## Slide 1: Computer Organization and Design
Chapter 2. Instruction: Computer Language
THE HARDWARE/SOFTWARE INTERFACE

## Slide 2: Instruction Struct
I
I
R
R
Format
lw
add immediate
sub (subtract)
add
Instruction
35
8
0
0
op
reg
reg
reg
reg
rs
reg
reg
reg
reg
rt
n.a.
n.a.
reg
reg
rd
n.a.
n.a.
0
0
shamt
n.a.
n.a.
34
32
funct
address
constant
n.a.
n.a.
address
I
sw
43
reg
reg
n.a.
n.a.
n.a.
address

## Slide 3: OPERAND
lw(Load Word)
g = h + A[8];
lw $t0, 32($s3)
add $s1, $s2, $t0
sw(Save Word)
A[12] = h + A[8];
lw $t0, 32($s3)
add $t0, $s2, $t0
sw $t0, 48($s3)
1
101
10
100
Data
0
4
8
12
Address
I
Format
lw
Instruction
35
op
reg
rs
reg
rt
n.a.
rd
n.a.
shamt
n.a.
funct
address
address
I
sw
43
reg
reg
n.a.
n.a.
n.a.
address
t0
t1
t2
t3
s0
s1
s2
s3
Base Address
(Register Value)

## Slide 4: Compile
Assembly Language
lw $t0, 1200($t1)
add $t0, $s2, $t0
sw $t0, 1200($t1)
Machine Language
100011 01001 01000 0000010010110000
000000 10010 01000 01000 00000 100000
101011 01001 01000 0000010010110000
A[300] = h + A[300];
43
0
35
op
9
18
9
rs
8
8
8
rt
8
rd
32
funct
1200
0
1200
address/shamt
sw
add
lw
Instruction

## Slide 5: Branch
if – then - else
if (i == j)
f = g + h;
else
f = g – h;
bne $s3, $s4, Else
add $s0, $s1, $s2
j Exit //jump to Exit
Else:
sub $s0, $s1, $s2
Exit:
beq(branch if equal)
beq register1, register2, L1
bne(branch not equal)
bne register1, register2, L1
while
while (save[i] == k)
i += 1;
Loop:
sll $t1, $s3, 2 //$t1 = i << 2
add $t1, $t1, $s6 // $s6 is base address
lw $t0, 0($t1)
bne $t0, $s5, Exit
addi $s3, $s3, 1
j Loop
Exit: